## Slide 1
OrbitWatch
Evidence-Grounded Spacecraft Telemetry Investigation
Final-semester research prototype
Measured experiment: nasa-full-seed17
Draft for supervisor review; not a publication or flight-readiness claim.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 2
Continuity with earlier work
Earlier project: spacecraft telemetry anomaly detection.
Summer study: Model Context Protocol integration.
Final deliverable: working detectors + traceable MCP investigation + measured results.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 3
Focused research question
Can evidence validation reject unsupported claims while retaining factual coverage?
Separate detection accuracy from explanation correctness.
A systems/experimental contribution, not a new neural architecture.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 4
System architecture
Recorded NASA data -> causal forecasters -> fixed thresholds.
Alert intervals -> structured evidence -> MCP tools.
Template or local LLM -> claim checks -> cited report.
Streamlit console, replay controls, local SQLite history.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 5
Data and evaluation discipline
81 channel files; 506,963 evaluated observations.
Chronological fitting/calibration; never concatenate channels.
No point adjustment; record false alarms, delay, and missed events.
Anonymous data and upstream test-extrema scaling are explicit limitations.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 6
Lightweight detectors
Rolling median versus GRU (hidden=24, window=32).
4 epochs; seed=17; CPU execution.
Threshold: calibration quantile 0.995.
Simple baselines may win; report measured outcomes honestly.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 7
Measured detection results
gru: macro F1=0.2162; AP=0.3175; event recall=0.8750.
rolling_median: macro F1=0.1582; AP=0.2610; event recall=0.6442.
Full per-channel measurements are included in detection_metrics.csv.
These scores are not comparable to point-adjusted F1 tables.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 8
Evidence instead of invented diagnosis
Each fact cites an evidence ID and a recorded numerical value.
Unknown fields, incorrect values, and invalid citations are rejected.
Physical root cause remains unknown.
Trusted rendering limits expressiveness but makes the boundary inspectable.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 9
Local explanation pilot
Model: qwen2.5:3b; paired complete/redacted evidence.
grounded_local_llm: unsupported=0.000; coverage=0.862.
ordinary_llm_plus_validator: unsupported=0.000; coverage=0.903.
ordinary_local_llm: unsupported=0.118; coverage=0.903.
template: unsupported=0.000; coverage=1.000.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 10
Live demonstration
Replay one channel and reveal a predicted alert.
Inspect observations, forecasts, and threshold ratios.
Investigate through a real MCP session and inspect its trace.
Export cited evidence; demonstrate refusal to invent a hardware cause.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 11
Limitations and next experiments
Single-seed detector study and a small claim-level explanation pilot.
No expert operator study or physical cause labels.
No claim of state-of-the-art or onboard certification.
Next: repeated seeds, expert evaluation, and external operational datasets.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.

## Slide 12
Deliverables
Executable local dashboard and MCP server.
Pinned environment, automated tests, and reproducible commands.
Trained local artifacts plus transparent measured result tables.
Technical report, presentation, and GitHub source.
Notes: Generated from actual experiment artifacts. Explain limitations and avoid claiming physical root-cause diagnosis.