## Slide 1
Indian Institute of Technology Jodhpur
AI-Based Spacecraft
Anomaly Detection
Using Multivariate Telemetry Time Series
Presented by: Vikash Malakar
Roll No: M25AI2155 | Supervisor: Dr. Shaily Verma | April 2026
Department of Computer Science and Engineering

## Slide 2
Presentation Outline
01
Introduction & Background
The spacecraft health monitoring challenge
02
Literature Survey
From thresholds to deep learning
03
Problem Definition
Formal problem and research objectives
04
Methodology
Datasets, models, and optimization
05
Results & Findings
Comparative performance analysis
06
Conclusion & Future Work
Summary and next steps

## Slide 3
Introduction & Background
13,883
Active satellites in orbit (2025)
85 TB
Daily telemetry from NISAR mission
1,000s
Sensor parameters per spacecraft
The Challenge
Traditional OOL (Out-Of-Limit) threshold methods are increasingly inadequate:
• Massive data volumes from modern missions
• Complex nonlinear sensor interdependencies
• Contextual anomalies missed by simple thresholds
• High-dimensional, noisy telemetry channels
Deep Learning Opportunity
Multivariate Time Series Anomaly Detection (MTSAD) models can:
• Learn complex temporal dependencies automatically
• Model spatial inter-sensor relationships
• Enable autonomous fault detection
• Support real-time decision making

## Slide 4
Literature Survey: Evolution of Methods
Threshold-Based
OOL limits
LSTM-NDT (NASA JPL)
Nonparametric Dynamic
Thresholding
USAD
Adversarial Autoencoder
Dual-decoder design
Amplifies anomaly
reconstruction error
TranAD
Transformer attention
Two-phase inference
Self-conditioning
Long-range dependencies
GDN
Graph neural network
Sensor as graph node
Relational anomaly
detection
Emerging
KambaAD (KAN+MAMBA)
LLM-based reasoning
Federated learning
Diffusion models

## Slide 5
Problem Definition
Formal Problem Formulation
Telemetry as multivariate time series: X = {x₁, x₂, …, xT} where xt ∈ ℝⁿ (n sensor readings at time t)
Goal: Learn mapping f : Wt → yt ∈ {0,1} where Wt is sliding window of past observations
🎯
Contextual Deviations
Values within limits but
behaving abnormally under
specific operational contexts
🔗
Relational Decoupling
Failures from disruption in
multi-sensor relationships,
not single sensor faults
📊
High Dimensionality
Thousands of heterogeneous
noisy telemetry channels
impossible to monitor manually

## Slide 6
Methodology: Datasets & Preprocessing
NASA SMAP
Soil Moisture Active Passive Satellite
55 Telemetry Channels
Parameter Categories:
Bus Voltage
HPA Current
Battery SoC
Temperature
RF Power Levels
NASA MSL
Mars Science Laboratory Rover
27 Telemetry Channels
Parameter Categories:
Gyroscope Readings
Reaction Wheel Speed
Internal Temps
Actuator States
Command Signals
Preprocessing: Min-Max Normalization + Sliding Window W_t = {x_(t-K+1), …, x_t} where K = window size

## Slide 7
Methodology: Model Architectures
USAD
UnSupervised Anomaly Detection
Architecture
Adversarial Autoencoder
How It Works
One encoder + two decoders in adversarial setup. Decoder 1 reconstructs normally; Decoder 2 is trained to fool Decoder 1. This amplifies reconstruction error for anomalous inputs.
⭐ Energy-efficient, stable baseline
TranAD
Transformer Anomaly Detection
Architecture
Transformer + Self-Conditioning
How It Works
Leverages attention to process time series in parallel. Two-phase inference: Phase 1 computes reconstruction error, which adjusts attention weights in Phase 2 for anomaly scoring.
⭐ Best for subtle contextual anomalies
GDN
Graph Deviation Network
Architecture
Graph Attention Network
How It Works
Each sensor is a graph node. Learns inter-sensor relationships dynamically. Anomaly = deviation of a sensor from its graph neighbors' predicted behavior.
⭐ Superior interpretability & root-cause

## Slide 8
Results: Comparative Performance
Dataset | Model | Precision (%) | Recall (%) | F1-Score (%)
MSL | USAD | 88.0 | 95.3 | 91.5
MSL | GDN | 92.1 | 91.9 | 92.0
MSL | TranAD | 91.2 | 97.4 | 94.2
SMAP | USAD | 87.5 | 98.1 | 92.4
SMAP | GDN | 93.2 | 93.8 | 93.5
SMAP | TranAD | 94.1 | 99.8 | 96.9
TranAD achieves best F1-score (96.9% on SMAP) — ideal for subtle anomaly detection
GDN leads in precision — modeling inter-sensor relationships reduces false positives
USAD is computationally efficient — viable for embedded/edge deployment

## Slide 9
Results: F1-Score Comparison
Chart: F1-Score (%) by Dataset
| USAD | GDN | TranAD
MSL | 91.5 | 92 | 94.2
SMAP | 92.4 | 93.5 | 96.9
Best Overall
96.9%
TranAD on SMAP
Best Precision
94.1%
TranAD on SMAP
Best Recall
99.8%
TranAD on SMAP

## Slide 10
Hardware-Aware Optimization
Goal: Enable on-board spacecraft deployment in resource-constrained embedded environments
RAM Reduction
Baseline
2.0 MB
▼
Optimized
59 KB
Reduction: 97.1%
Compute (MACs)
Baseline
100%
▼
Optimized
0.6%
Reduction: 99.4%
Accuracy Drop
Baseline
92.7%
▼
Optimized
88.8%
Reduction: −3.9%
Key Insight: Significant reductions in memory (97.1%) and compute (99.4%) are achievable with only a modest 3.9% accuracy trade-off — making AI-based anomaly detection feasible for deployment on spacecraft embedded systems.

## Slide 11
Interpretability & Root-Cause Analysis
Why GDN Excels at Interpretability
GDN treats each sensor as a node in a learnable graph. Edges represent learned relationships between sensors.
When an anomaly occurs, GDN identifies WHICH sensor relationship was disrupted — not just that something is wrong.
This is critical in mission-critical systems where knowing the source of failure is as important as detecting it.
Sensor Graph: Anomaly = edge disruption detected
USAD & TranAD: detect anomalies but cannot explain which sensor caused it.
GDN:
pinpoints the exact sensor relationship that was disrupted, enabling targeted fault isolation.
Graph Representation of Sensor Relationships
Gyro
React.
Wheel
Battery
RF
Power
Temp
Sensor
Nodes = Sensors | Edges = Learned Relationships | Red edge = Anomaly detected

## Slide 12
Summary & Future Work
Key Findings
TranAD:
Best detection performance (F1: 96.9%) — captures subtle contextual anomalies
GDN:
Best interpretability — graph-based root-cause analysis
USAD:
Most computationally efficient — energy-aware design
Optimization:
97.1% RAM, 99.4% compute reduction with only 3.9% accuracy loss
Future Directions
MAMBA / KAN:
State-space models for efficient long-sequence modeling
LLM Integration:
Semantic, human-readable anomaly explanations
Federated Learning:
Collaborative multi-spacecraft training without raw data sharing
Diffusion Models:
Improved normal-behavior modeling for higher detection accuracy
This work advances autonomous, interpretable, and hardware-efficient AI health monitoring for future space missions.

## Slide 13
Thank You
Questions & Discussion
Vikash Malakar | M25AI2155 Supervisor: Dr. Shaily Verma Dept. of CSE, IIT Jodhpur | April 2026